## Slide 1: Let’s begin your MRI journey!
CHU Poitiers
LabCom CNRS I3M
DACTIM-MIS, Laboratoire Mathématiques et Applications CNRS 7348, Université de Poitiers
Mathieu NAUDIN
Mathieu.naudin@chu-poitiers.fr

## Slide 2: Who I am?
PhD thesis at Siemens Healthineers (2015-2018)
  XLIM as main research center
  Collaboration with LMA and CHU de Poitiers
Research engineer at CHU Poitiers
  Responsible of 7 Tesla magnet engineering
  Responsible of AI platform of I3M lab
Thanks to MR physicist Carole Guillevin and MR AI engineer Pierre Fayolle for their help
(and some of their slide for this course)

## Slide 3: Course overview
Generalities in health domain : data format
MRI principle
Preprocess MRI data

## Slide 4: Global objective of the class
Globally understand the MRI principle and the associated technology
Be able to work with medical MR data/imaging

## Slide 5: Objectives of today’s class
Overview of MR technology and communication (DICOM)
A brief introduction to MR physics
Work with real MR data and associated k-Space

## Slide 6: Exchange time!
What do you know about medical imaging ?

## Slide 7: Introduction
Welcome in the medical image jungle!

## Slide 8: Introduction
Typical Architecture of an imaging structure private or public

## Slide 9: Introduction
Have a closer look to the previous items:
- RIS : Radiology Information System for the patient/appointement/ data management
- PACS : stands for Picture Archiving and Communication System, this is the location where images are stored(DB)

## Slide 10: Introduction
- Scanner/Sources : A large number of sources can generate images. They can be original or secondary (captures, documents, AI results, etc)
- Users : a large number of people are inside these systems : radiologists, technologists, clinicians, etc.
⇒ Simpliest example !

## Slide 11: DICOM
This is the Universal format of medical imaging
Old one: 1985
Proposed by :
  ACR : American College Of Radiology
  NEMA : National Electric Manufacturers Associations
It is not only an imaging format :
  Communication protocole TCP/IP
  Images format
Increase the inter-constructor operability by a format thant can be adopted by everyone

## Slide 12: DICOM
Now, in its third version from … 1993
Adding several items along the years : version 3
Small evolution are added every years, no version 4 planned for the moment

## Slide 13: DICOM
it is also a display format for medical data.
It appears in the form of a Looking Up table (LUT) thanks to the DICOM Grayscale Standard Display Function (GSDF) function.
Specific charts are used for calibration and screen verification.
Barten’s Curve

## Slide 14: DICOM
Format is now HUGE
  22 parts
  More than 3500 tags referenced
  Didn’t take into account the private tags from constructors
Complex drift requiring a good understanding of the structure

## Slide 15: DICOM Objects
CR
CT
MR
NM
SC
US
US multi
XA
XA bi
XRF
Computed Radiography Imaging
Computed Tomography Imaging
Magnetic Resonance Imaging
Nuclear Medicine Imaging
Secondary Capture Imaging
Ultrasound
Ultrasound Multi-fame Imaging
Angiographic Imaging
X-Ray Angiographic Bi-Plane Imaging
X-Ray Radiofluoroscopic Imaging

## Slide 16: DICOM Services Classes
1. Verification
2. Modality Worklist Management
3. Performed Procedure Step [PPS]
4. Store
5. Storage Commit
6. Print
7. Query/Retrieve

## Slide 17: Storage and Storage Commit
Both are transfering images
But, in the commitment, the ownership is transferred and the image could be safely deleted from the Object

## Slide 18: SCU and SCP
SCU
Service Class user
Client
SCP
Service Class Provider
Server
SOP
Service Object Pair
MR Image Storage SOP Class

## Slide 19: SOP

## Slide 20: Machine negociation
<Request>
<Response>
MR Image Store SOP Class
FOR EACH dicom file generated
AE_T 1
AE_T 2

## Slide 21: Information model
Divided into several subparts
  A Patient
    Several Study
      Divided into several series
        That contains several instances
Study
  Asked as initial protocol
Series
  MRI sequences done by the technologist

## Slide 22: Mandatory UID
SOP Class UID Identify : the service type/object to the storage location
Study Instance UID : Identify a full examination (location and time)
Series Instance UID : Identify a image series from study
SOP Instance UID : Identify image associated to the file

## Slide 23: DICOM

## Slide 24: DICOM
But … where is the image in this jungle ?
It is hidded in the Pixel Data Tag
Tags needed to fully use the pixel data :
  Rows and Columns
  Samples Per Pixel
  Photometric Interpratation
  Planar configuration
  Bits Allocated, Bits Stored and High Bit
Image size computing:
ROWS * COLUMNS * NUMBER_OF_FRAMES *
SAMPLES_PER_PIXEL * (BITS_ALLOCATED/8)

## Slide 25: NIFTI
Neuroimaging Informatics Technology Initiative
This is a neuroimaging format that is still in its early stages.
Unlike DICOM, it uses a single file to group files.
NIFTI is available in two versions - NIFTI-1 and NIFTI-2 - which allow for superior storage.
Additionally, there is a difference in reference between DICOM and NIFTI

## Slide 26: NIFTI
With two mains differences: LPS (DICOM) et RAS (NIFTI)

## Slide 27: NIFTI
Composed by a simple header (less complex than the DICOM)
Then, a data matrix (with all slices)
Contains also transformation matrix
Useful Python library: Nibabel

## Slide 28: Other formats

## Slide 29: Other formats
.hdr / .img / .rda / .npy
There is a large, large number of different medical imaging format
Advice : Try to come back as possible to something you know
  Helps in using well known tools (software, etc.)
  Re-use that you coded before for this specific type
  Will smooth the imaging transfert part
Don’t be lost in file format jungle

## Slide 30: Quizz
To see if everything is ok!

## Slide 31: Question 1 : modality ?

## Slide 32: Question 2 : modality ?

## Slide 33: Question 3 : modality ?

## Slide 34: Question 4 : modality ? Pathology ?

## Slide 35: Question 5 : modality ? Pathology ?

## Slide 36: Question 6 : modality ?

## Slide 37: Question 7 : modality ? Ponderation ?

## Slide 38: Question 8 : modality ? Ponderation ?

## Slide 39: Question 9 : modality ? Ponderation ?

## Slide 40: MR Generalities

## Slide 41: Exchange time!
What do you know about MR ?

## Slide 42: Historic
Starting from 1930, the physicist Isidor Isaac Rabi took an interest in the nature of the forces that bind protons in the atomic nucleus.
  He pioneered molecular detection through a magnetic resonance system.
1933 Stern et al. discovered that the proton possesses a magnetic moment.

## Slide 43: Historic
Magnetic field
  In 1939, I. Rabi demonstrated the interaction of electromagnetic waves and nuclei on beams of atoms, discovering the phenomenon of magnetic resonance (Nobel Prize in Physics)
  In 1946, the description of magnetic resonance imaging (MRI) on samples of water or paraffin was independently provided by F. Bloch (West Coast) and E. Purcell (East Coast).
    The behavior of the proton in a magnetic field led to the Nobel Prize in Chemistry in 1952

## Slide 44: Historic
NMR Spectroscopy
  1950-70
    he phenomenon of magnetic resonance was first used by physicists and chemists to characterize matter through spectra..
      Protor and Yu discovered the frequency shift depending on the molecular environment, turning NMR into an analytical chemistry tool.
      Développement de la spectroscopie par RMN
    NMR spectroscopy was further developed, with the first NMR signal recorded by Hahn, and the advent of superconducting magnets

## Slide 45: Historique
MR Imaging
  1971 Difference in NMR signal between normal and cancerous tissues: Robert Damadian
  1972 Peter Mansfield developed mathematical formulas for faster MRI acquisitions
  1973 Paul Lauterbur created a system capable of producing a virtual cross-sectional image of an object :
    introducing gradients
    producing the first images of two test tubes.
from Nature 1973; 242: 190- 191

## Slide 46: Historique
MR Imaging
  1974 Paul Lauterbur (USA) and Peter Mansfield (GB) obtained the first images of a living animal by MRI (Nobel Prize in Physics in 2003)
  1977 Premières images RMN humaines : Moor, Hinsaw-Mansfield
C'est à partir de ce moment que l'idée d'introduire la RMN en tant qu'imagerie médicale naît.

## Slide 47: MR components

## Slide 48: MRI machine

## Slide 49: MRI machine

## Slide 50: Quench of a MRI magnet
Quench = Sudden transition from liquid helium to gaseous state due to its heating due to malfunction of the thermal insulation system or caused by the safety punch.
It leads to a loss of superconductivity and therefore of the main magnetic field.

## Slide 51: Magnet = strong magnetic field!
Attention to ferromagnetic objects!
DANGER for people with pacemarkers, metal implants

## Slide 52: Magnet
Bo
Bo

## Slide 53: RF system
The RF system is made up of:
  One or more RF generators.
  Homogeneous RF antennas for excitation.
  Sensitive RF antennas for signal reception.
  Pre-amplifiers and amplifiers.
  Analog-to-digital converters.

## Slide 54: RF generator
The RF generator produces current pulses of variable shape oscillating around the resonance frequency.
Risks associated with RF:
  RF energy absorption in tissues can produce local heating.
SAR (Specific Absorption Rate) = power deposited relative to the patient's weight
SAR < 10 W/kg for the whole body
SAR < 1.5 W/kg for the head

## Slide 55: RF antennas
Antenna = resonant RLC circuit
Copper coil in different shapes
Tuned to the proton resonance frequency and impedance-matched to electronic circuits
Antenna tailored to the sample size to increase the signal-to-noise ratio (S/N)
Antennas are only receivers
The RF transmission is done by the integrated antenna between the machine chassis and the magnet

## Slide 56: Coils
Surface coils
Surface coils are applied as close as possible to the regions being imaged.
Surface coils favor a high signal-to-noise ratio.
Volumic coils
Volume coils can encompass a region of the body (e.g. head, knee) or the entire body (whole-body coil).
Volume coils allow for a homogeneous signal across the entire imaged volume..

## Slide 57: Gradient
The gradient system consists of
  High-performance current generator.
  Coils generating gradients in the three directions.
  Coils for correcting gradient linearity.
  A vibration-damping resin mold (for acoustic noise reduction).
  A cooling water circuit.

## Slide 58: Gradient coil

## Slide 59: Gradient - Caraxteristics
The performance of gradients for spatial encoding of the signal is related to:
Their maximum amplitude (variation of magnetic field in mT/m), which determines the maximum spatial resolution (slice thickness and field of view).
Their slope, which corresponds to their switching speed. A high slope is necessary to quickly switch the gradients and enable ultra-fast imaging sequences.
Their linearity, which must be as perfect as possible within the field of view.

## Slide 60: Les gradients - Caractéristiques
Eddy currents
  During the rise and fall of gradients, induced currents can be created in conductive materials near the gradient coils (cryogenic envelope, electrical wires, antennas, shimming coils...).
  These induced currents (eddy currents) will oppose the gradient field and degrade their profile.

## Slide 61: Gradients - Caracteristics
To counteract these induced currents, several methods are employed:
  Active shielding of gradient coils.
  Optimization of the profile of the electric current sent to the gradient coils during the rise and fall to compensate for eddy currents.
  Gradient switching generates Lorentz forces that cause vibrations in the gradient coils and their supports.
  These vibrations are the main source of the characteristic noise of MRI.

## Slide 62: Gradient – level : clinic

## Slide 63: Gradients – Level : expert

## Slide 64: MR Signal

## Slide 65: Spin
Spin is a fundamental property of particles, such as protons, that have a magnetic moment. It refers to the intrinsic angular momentum of the particle and can be thought of as its intrinsic spin.
Larmor frequency is the resonant frequency at which particles with a magnetic moment precess in a magnetic field. It is proportional to the strength of the magnetic field and the gyromagnetic ratio of the particle.
P+
n°
I

## Slide 66: Les noyaux utilisables en RMN
Nuclei Nmber I Natural abundance. Sensibility Larmor frequency
% (MHz/T)
H1 ½ 99.98 1 42.576
H2 1 0.015 0.0096 6.535
P31 ½ 100 0.0664 17.236
F19 ½ 100 0.834 40.055
C13 ½ 1.108 0.0159 10.705
N15 ½ 0.365 0.00104 4.315
O17 5/2 0.037 0.0291 5.772

## Slide 67: Le noyau d’hydrogène
In the human body, 75% is water.
  2 hydrogen atoms per water molecule.
  Hydrogen atoms represent 2/3 of the atoms in the body.
  The hydrogen atom has a single proton with a very high magnetic moment.
In NMR, the nomenclature used is spins and protons.

## Slide 68: Le phénomène RMN peut être décomposé en 3 étapes
1- Polarization
2- Resonance
3- Relaxation
NMR: studying the magnetization changes of the nuclei of a substance under the joint action of two magnetic fields:
A fixed and high static magnetic field Bo:
  Equilibrium state.
A rotating electromagnetic field B1:
  Perturbation state.

## Slide 69: Polarization
It occurs during the introduction of the patient into the B0 magnetic field.
B0 magnetic field
Natural environment
Notes: Pour un vecteur individuel dans Bo, création d’un moment magnétique u = gamma *spin.
Moment cinétique peut etre quantifié C = gamma * Bo -> moment magnétique quantifié alors le vecteur peut prendre que certaines directions ( parallèles et antiparallèles à Bo)
Les vecteurs aimantations microscopiques adoptent un mouvement de précession autour de Bo w= gamma Bo
Pour une population de vecteur

## Slide 70: Polarization
B0
Parallel
Anti Parallel
To be more precise, the spins are distributed on a cone of axis B0, with an excess of spins oriented parallel to B0 (Boltzmann distribution).
This induces the appearance of a macroscopic magnetization vector M0 parallel to B0: the longitudinal component Mz0.
M0 corresponds to the vector sum of all the spins.
Mz0 increases as the magnetic field B0 increases.
Spins are dephased.
Mz0
+1/2
-1/2

## Slide 71: ResoNance
!!! Equilibrium state: Impossibility to measure Mz !!!
No signal.
Perturbation is inducted by energy !
z
x
y
Mz
B1
B0

## Slide 72: ResoNance
Emmiting antenna
Antenna = resonant circuit (R, L, C)
B1 field delivered by the antenna perpendicular to Bo.
Tuned to the resonance frequency of the proton. Impedance matching to the electrical circuits.

## Slide 73: ResoNance
Disturbance of the equilibrium state
The macroscopic magnetization M rotates by an angle α proportional:
To the amplitude of the emitted B1 field
To the duration of the emission τ.
B0
Mo
B1

Emitting coil
M
α = γ.B1.

## Slide 74: Relaxation
Relaxation characterizes the return to equilibrium of the spin system.
It begins when the RF wave B1 stops => exchange of energy with the environment.
B0
E
½ E
-1/2 E
Mxy

## Slide 75: Longitudinal relaxation – T1
When B1 stops, two phenomena occur:
Longitudinal relaxation characterizes the return of magnetization along Bo.
Return of an excess of protons in the parallel direction to Bo.
It is define by the longitudinal relaxation : T1
Mz = Mo [1-exp (-t/T1)]
Mz
Temps t
Mo

## Slide 76: Longitudinal relaxation – T1
T1 is long and specific to each tissue and not constant over time
The T1 of a tissue is the time it takes for it to achieve 63% of its T1 relaxation.
T1 depends on the properties of hydrogen nuclei contained in different tissues.
T1 varies depending on the tissues.

## Slide 77: Transversal relaxation - T2
When B1 stops, two phenomena occur:
The longitudinal relaxation characterizes the recovery of the magnetization along the z-axis.
The transverse relaxation characterizes the decay of transverse magnetization.
Redephasement of spins relative to each other occurs during transverse relaxation.
It’s define by the T2 relaxatoon time
Mxy = Mo exp (-t/T2)
Mxy
Temps t
Mo

## Slide 78: Transversal relaxation - T2
Fast, tissue-specific, and not constant over time.
The T2 of tissue is the time at which the tissue has undergone 63% of its T2 relaxation. This means that 37% of the transverse component remains.
T2 depends on the interactions between hydrogen nuclei in different tissues, and varies depending on the tissue type

## Slide 79: Transversal relaxation - T2*
If there are field inhomogeneities in the sample, spins will not precess at the same frequency f0
An additional phase shift is required to obtain the true T2, using a 180° pulse.
The decay of transverse magnetization is then faster: T2*.
Temps t
Mo
T2
T2*
Mxy

## Slide 80: Signal reading
B0
The collected signal S is a Free Induction Decay (FID)
S = So sin (2π.fo.t) exp(-t/T2)
S0
Signal
Temps
T2 ou T2*
Oscillations à la fréquence fo
Relaxation transverse
The FID decreases like T2, but in reality it decreases more rapidly due to field inhomogeneities.

## Slide 81
Imperfect magnetic field + current in the shim coils
Result : FID longer more T2 than T2*
B0 non homogeneous
B0 homogeneous

## Slide 82: Signal to image

## Slide 83: Gradients
To form an image, it is necessary to localize in space the signal received by the antenna.
This is possible thanks to the use of magnetic field gradients applied in the three planes of space at different times during the sequence.

## Slide 84: 3D encoding
Tac = TR ∙ NPy ∙ NPz ∙ Nex
With
TR = repetition time
TE = echo time
NPy = Number of encoding steps in the y-axis.
NPz= Number of encoding steps in the y-axis
Nex= Number of averages

## Slide 85: Gradients : spatial encoding
The spatial encoding relies on the successive application of magnetic field gradients.
A slice selection gradient (GSS) is applied to select the anatomical volume/slice to be explored.
Inside this volume, the position of each point is encoded vertically by applying a phase encoding gradient (Gφ) and horizontally by applying a frequency encoding gradient (Gω).
The different gradients have identical properties but are applied at distinct times and in different directions.

## Slide 86: Total scan duration
Tac = TR x Nlines x Nex

## Slide 87: Sequence
A pulse sequence is like a music score for protons.
The ingredients are not notes but RF pulses, gradient pulses, and delays.

## Slide 88: From signal to image
When the system recovers the signal, it fills a mathematical space called Fourier space or k-space.
This k-space will contain all the information necessary for the formation of the image.
The k-space is transformed into the image through a double Fourier transform, and the image is transformed back into Fourier space through a double inverse Fourier transform.

## Slide 89
From signal to image
Fourier Transform
Fourier Transform -1
Image Space
K-Space
Frequency

## Slide 90: From signal to image– k-Space and Fourier Transform
TF
Ky
Kx

## Slide 91: From signal to image– k-Space and Fourier Transform
K-space filling could be : radial, linear, spiral …

## Slide 92: Preprocessing and artifacts

## Slide 93: Preprocessing
CT Scan
Semi-quantitative (Unité d'Hounsfield)
Fast and without motion artifacts
Registration required
MRI
Absence of intensity standardization
Artifact in the K-space
Real need for standardization between machines

## Slide 94: Preprocessing
L’ensemble des traitements de données avant l’apprentissage ou calcul
Nécessite que les données soient correctement acquises

## Slide 95: Data heterogeneity
Different vendors, machines et fields
  Siemens, Canon, GE
  1.5 Tesla, 3 Tesla, 7 Tesla
Different acquisitions :
  Intensity, FOV voxel size…

## Slide 96: Data heterogeneity
3T versus 7T : contrasts …
3D FLAIR
Magnetom 3T Skyra (Siemens)
3D FLAIR
Magnetom 7T Terra (Siemens)

## Slide 97: Preprocessing
Data transformation
Data cleaning
Data augmentation
Data profiling
Data validation

## Slide 98: Preprocessing
Data must be standardized
  Same same
  Same tissular response
   Better for computation and AI prediction
B0 Correction
SimpleITK, FSL
Brain extraction
FSL, BSE, ROBEX
Registration
SimpleITK, FSL

## Slide 99: Main artifacts
Multiple artifacts : patient movements, acceleration (PAT)
Susceptibily artifacts : effect of susceptibilité…
Implanted devices artifacts : black hole, etc…
Spikes
Ghosting
Movement
Susceptibility

## Slide 100: Main artifacts
Donald W. McRobbie, Elizabeth A. Moore, Martin J. Graves, Martin R. Prince - MRI from Picture to Proton (2017, Cambridge University Press)

## Slide 101: Preprocessing
Especially for MRI data
  Noise reduction
  Bias field correction (B0)
  Registration : to an atlas, to a reference
  Slicing, interpolation
  Standardization : Combat, histogram matching…
B0 Correction
SimpleITK, FSL
Brain extraction
FSL, BSE, ROBEX
Registration
SimpleITK, FSL

## Slide 102: Preprocessing
Biais field correction :
  Reduce B0 field inhomogeneity
Correction B0
SimpleITK, FSL
Raw image
B0 field
Corrected Image
“B0 mapping”

## Slide 103: Preprocessing
Registration
SimpleITK, FSL
Registration :
  Aligning an image to a reference image or atlas
  "Non-linear registration" vs "linear registration"

## Slide 104: Preprocessing
"Brain Extraction Tool" (BET) or "Skull Stripping"
  Removal of all non-brain tissues
  Subcutaneous fat
  Muscular tissues
  Cranial box
Brain extraction
FSL, BSE, ROBEX

## Slide 105: Preprocessing
Data augmentation
  Le nombre de données est souvent très limitant pour l’apprentissage
  The dataset is most of the time limitated
  Generation of new images from the current dataset (roattation, scaling, morphing, blurring)
  “TorchIO”
Idea of giving to AI or pipeline the closest data from reality
F. Pérez-García, R. Sparks, and S. Ourselin. TorchIO: a Python library for efficient loading, preprocessing, augmentation and patch-based sampling of medical images in deep learning. Computer Methods and Programs in Biomedicine (June 2021), p. 106236. ISSN: 0169-2607.doi:10.1016/j.cmpb.2021.106236.

## Slide 106: Expert libraries
TorchIO
MONAI Framework (Nvidia)

## Slide 107: Quizz
Oh no! Not again …

## Slide 108: Preprocessing – Name the artifacts
Image originale
Flou aléatoire

## Slide 109: Preprocessing – Name the artifacts
Pivotement aléatoire
Bruit aléatoire
Transformation d’affine aléatoire
Déformation aléatoire

## Slide 110: Preprocessing – Name the artifacts
Biais de champ aléatoire
Mouvement aléatoire
Spikes aléatoires
Ghosting aléatoire

## Slide 111: Merci de votre attention !